Guangzhou LEVA Packaging Equipment Co.,Ltd.

Optical laser printing machine

LPE-OLP030

Technical Parameters：

1.Laser power:10W/20W/30W

- Laser wavelength:1064nm

- Laser output power:10%~100% continuously adjustable

- Laser output frequency:20KHz~100KHz continuously adjustable

- Power stability:<±1%rms

- Focus spot diameter:<0.01mm

- Marking range:150mm*150mm

- Optional range:50mm*50mm  100mm*100mm  200mm*200mm

- Marking depth:≤1.2mm

- Marking speed:800 standard characters/second

- Minimum line width:0.012mm

- Minimum character:0.15mm

- Repeatability:±0.003mm

- Cooling method:Air cooled

- Power supply :220V  50/60Hz   <400W

- Laser module life:100000 hours

- System operating environment:WindowsXP/2000/98