Guangzhou LEVA Packaging Equipment Co.,Ltd.

Pressure sensitive labeler for can body

LPE-LFB30

Technical Parameters：

Labeling speed: about 0-60P/min
Labeling accuracy:±1mm（Does not include errors such as product labels）
Applicable bottle size:Diameter 30-150mm；Height 30-350mm；
Applicable labeling size:Length 10～260mm,backing paper width 10-160mm
Max. Applicable label: outer diameter within 300mm，inner diameter 76mm
Ambient temperature /humidity:0-50℃/15-85%
Power supply：AC220V, 50HZ       
Size:L2200*W1300*H1700mm

Weight:about 190kg        

Label Requirements
Labels spacing：2-3mm±0.2mm
Label feeding method is coil material
Material: It is recommended to use glassine backing paper, avoid cuts, affecting the normal operation of labeling